## Slide 1: New examples of encoding satellite geolocation information
Edward Armstrong1, Sasha Ignatov2, Matt Pennybaker2, and Wen-Hao Li1
1. Jet Propulsion Laboratory, California Institute of Technology
2. NOAA STAR.
© 2019. All rights reserved.
California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Implementations of novel geolocation encoding for Level 1and 2 satellite data
Implementation #1
  Encoding geolocation for the geostationary GOES-16 (aka “GOES R”) platform
    GOES ABI (sensor) for atmospheric and oceanographic observation
    New technique leveraging CF projection information for the NOAA GHRSST L2P SST dataset
      https://podaac.jpl.nasa.gov/dataset/ABI_G16-STAR-L2P-v2.70
Implementation #2
  Encoding geolocation for polar orbiting NPP VIIRS sensor
    Multispectral VIIRS used for all manner of earth atmosphere, land and ocean observation. MODIS follow-on.
    Eumetsat has developed pixel level interpolation technique to retrieve subsampled L1 geolocation points

## Slide 3: Leveraging CF for geostationary SST datasets
The Group for High Resolution SST (GHRSST) has a specific data model for encoding Level 2 geolocation latitude and longitude
  Every pixel is assigned its unique lat/lon
  lat/lon information stored as floats; “heaviest” variables in the granule suite
  See the GDS reference documentation
    https://podaac-tools.jpl.nasa.gov/drive/files/allData/ghrsst/docs/GDS20r5.pdf
The geostationary view of the observation “disk”, essentially a unprojected grid, lends itself to encoding using a map projection which is possible using the “grid_mapping” CF metadata attribute referencing
  grid_mapping_name = "geostationary" ;
How does this look like and perform? …….

## Slide 4: Existing L2P GHRSST encoding
Example NetCDF CDL from previous version of the GOES-16 dataset
dimensions:
ni = 5424 ;
nj = 5424 ;
time = 1 ;
float lat(nj, ni) ;
lat:standard_name = "latitude" ;
lat:units = "degrees_north" ;
lat:valid_max = 90.f ;
lat:valid_min = -90.f ;
float lon(nj, ni) ;
lon:standard_name = "longitude" ;
lon:units = "degrees_east" ;
lon:valid_max = 180.f ;
lon:valid_min = -180.f ;
short sea_surface_temperature(time, nj, ni) ;
sea_surface_temperature:add_offset = 273.15f ;
sea_surface_temperature:coordinates = "lon lat" ;
sea_surface_temperature:scale_factor = 0.01f ;
sea_surface_temperature:standard_name = "sea surface sub-skin temperature" ;
sea_surface_temperature:units = "kelvin" ;

## Slide 5: New L2P GHRSST encoding
Example NetCDF CDL from new version of the GOES-16 dataset
dimensions:
time = 1 ;
nj = 5424 ;
ni = 5424 ;
float nj(nj) ;
nj:axis = "Y" ;
nj:units = "radians" ;
nj:standard_name = "projection_y_coordinate" ;
float ni(ni) ;
ni:axis = "X" ;
ni:units = "radians" ;
ni:standard_name = "projection_x_coordinate" ;
short sea_surface_temperature(time, nj, ni) ;
sea_surface_temperature:add_offset = 273.15f ;
sea_surface_temperature:coordinates = "nj ni" ;
sea_surface_temperature:scale_factor = 0.01f ;
sea_surface_temperature:standard_name = "sea surface sub-skin temperature" ;
sea_surface_temperature:units = "kelvin" ;
sea_surface_temperature:grid_mapping = "geostationary" ;

## Slide 6: CF projection information
NetCDF CDL from new version of the GOES-16 dataset
int geostationary ;
geostationary:grid_mapping_name = "geostationary" ;
geostationary:semi_major_axis = 6378137. ;
geostationary:semi_minor_axis = 6356752.314245 ;
geostationary:inverse_flattening = 298.257223563 ;
geostationary:latitude_of_projection_origin = 0. ;
geostationary:longitude_of_projection_origin = -75. ;
geostationary:false_easting = 0. ;
geostationary:false_northing = 0. ;
geostationary:horizontal_datum_name = "WGS_1984" ;
geostationary:reference_ellipsoid_name = "WGS 84" ;
geostationary:prime_meridian_name = "Greenwich" ;
geostationary:geographic_crs_name = "WGS 84" ;
geostationary:sweep_angle_axis = "x" ;
geostationary:perspective_point_height =

## Slide 7: Plotting with Panoply

## Slide 8: Granule data reduction → greater than 80% !!
Average: 272 MB → 44 MB

## Slide 9: Eumetsat L2 VIIRS compact data model

## Slide 10: VIIRS Compact data model
1 INTRODUCTION
1.1 Purpose
During the implementation of the EUMETSAT provided VIIRS Regional Service (EARS-VIIRS) a need was identified to develop a Compact VIIRS SDR Product Format (Level 1) to achieve a cost efficient distribution of the VIIRS data via EUMETCast, EUMETSAT’s satellite based data distribution system.
This document specifies the Compact VIIRS SDR Product Format and how it relates to the Original VIIRS SDR Product Format developed as part of the Suomi-NPP and JPSS Programmes. It provides guidelines on how to construct the Compact product format from the Original product format and on how to reconstruct the Original product format from the Compact product format.

## Slide 11: VIIRS Compact data model
In the Compact VIIRS SDR format, geolocation data is stored only for the corner points, i.e. the Tie-Points, of each Tie-Point Zone. Interpolation functions are defined for re-constructing the geolocation data for all pixels within the Tie-Point Zone.

## Slide 12: Original layout

## Slide 13: Tie point example

## Slide 14: The Tie Point grid

## Slide 15: Reconstruction of Original Longitude and Latitude
Each Tie Point set, with lon/lat for corners A,B,C,D and alpha representing satellite zenith angle

## Slide 16: Summary
CF provides an elegant roadmap for encoded geolocation geostationary L1 and L2 observations by leveraging projection information similar to an L3 grid
  80% data reduction
  But coordinates in original radians format
Eumetsat has developed a data model to decimate original obs keeping a subset of tie points and then interpolate back the geolocation information for L1 polar orbiting satellites
  Substantial size reduction. Probably an order of magnitude
  But interpolation needed to retrieve original geolocation values
  Have any software developers tackled this ?
What else is on the horizon ?
Disclaimer: Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise, does not constitute or imply its endorsement by the United States Government or the Jet Propulsion Laboratory, California Institute of Technology.