## Slide 1
Eel River CZO
Data Management & Dendra
dendra.science
Eel River
criticalzone.org/eel
angelo.berkeley.edu
J. Scott Smith
Software Architect,
New Leaf Solutions
Collin Bode
Data Manager
Eel River CZO
CA Heartbeat Initiative
UC Natural Reserves

## Slide 2
Angelo Coast Range Reserve
UC Natural Reserve System
Eel River, CA
Angelo
Sagehorn
Ranch
Eel River
Approach: where are we?
Notes: Largest mostly undammed river in CA. Short, steep, rapidly eroding in soft sedimentary rock of the CA coastal range.

## Slide 3
evaporation
transpiration
zb
transpiration
Rock Moisture: a possibly dominant source of water storage in the CA coastal range
Approach: what is our research?
Eel River
The Unmeasured Zone: the unsaturated weathered bedrock through which meteoric water passes to the groundwater
Critical Zone in erosional landscapes

## Slide 4
Rivendell
Cahto Peak
HQ
Angelo
Meadow
South Meadow
Soil Moisture
North
East
Stilling Well
USGS
Gage
Approach: Intensive Monitoring
Eel River
Real-time Sensor Observatory
Sensor Observatory
High speed wireless network
All equipment online
5 minute interval
Most monitoring on one hillslope
Notes: Image of the Reserve and Rivendell

## Slide 5
Tools: Trees for power and communication
Peter Steel, Reserve manager

## Slide 6
Redwood height: 40 meters
Solar System total weight: 80kilos
Arms: very sore
Networks: REB Construction

## Slide 7
Eel River
Equipment Type: Campbell Scientific

## Slide 8
Vadose Zone Monitoring System: two 19 m long sleeves in 55 degree (from horizontal) inclined holes. One hole-TDT moisture and lysimeters every 2 m; other hole- 2 m long lysimeters to capture fracture flow and tubes to collect gas at each interval depth. Installed October 25, 2015
Vadose Zone Monitoring System

## Slide 9
Rivendell Sensor List
Value Measured | Instruments
Barometric pressure | 8
CO2 Sensor | 2
Light, net radiometer | 1
Light, shortwave | 14
Light, shortwave, offline | 30
Logger, battery voltage | 21
Logger, temperature | 21
Precipitation, tipping bucket | 9
Relative humidity | 21
Sap flow | 136
Snow pack height, sonic | 1
Soil Hygrometer/Psychrometer | 54
Soil moisture, Electrical resistance | 192
Soil moisture, sm200 | 30
Soil moisture, time domain reflectometer | 100
Temperature, air | 21
Temperature, air, offline | 30
Temperature, water | 3
Water content reflectometers | 15
Water samples, isco | 4
Water turbidity | 1
Well and stream water level | 23
Well water level, manual | 12
Wind, direction | 6
Wind, speed | 7
Total | 792
Eel River
Notes: scaling issues with large numbers of sensors. reliability becomes more important than cost. online critical.

## Slide 10
Goal: to provide a system to actively manage both the data and the equipment in a sensor observatory
Features
Station dashboards
Datastream Query & Graphing
System Status
Dynamic Versioning of Data
Software stack
Node.js
Vue interface
MongoDB
Time-series DB independent
  InfluxDB
  MySQL
Stats
3 Organizations
50 Stations
2000 Datastreams
1.2 Billion Datapoints

## Slide 11
http://dendra.science
Live System Status

## Slide 12
http://dendra.science
Individual Station Dashboards

## Slide 13
http://dendra.science
Datastream Query Interface

## Slide 14
http://dendra.science
Datastream Graphing Interface

## Slide 15
http://dendra.science
Datastream Graphing Interface

## Slide 16
Incident ID: 5c8716bef191e048cac27c84
Title: Ant Colony Corrodes Radio
Station: Ingrid Tree Weather Station
Datastreams: resistance probes,
rain collector
wells
Data Flagged: ERPs: 90,304 values
Well 6: 3,024 values
Well 7: 3,024 values
Flag: NETWORK FAILURE, VALID
Begins_at: 2014-03-24
Ends_before: 2014-04-08
Submited_by: Collin Bode
Submited_at: 2014-04-09T00:00:00Z
Description:
Okay, I wasn't expecting that. I climb 40 meters up a Ingrid (douglas fir tree) to figure out why my data logger's wireless stopped working. I open the box, and surprise! An ant colony is using the wireless radio as an egg warmer.
The colony somehow corroded the connectors between the radio and the logger so badly that the firmware got corrupted. All slave radios were offline until I replaced the radio a spare. I left the box open to allow them to naturally disperse, then swept the stragglers out with a paintbrush. Replugged the hole with weather goop.
http://dendra.science
Incident Reports (annotations)

## Slide 17
http://dendra.science
Dynamic versioning of datasets
Flag and Translate System
User submits a report
Annotation is processed
Source data is unchanged
All data pulled is now translated
  Invalid flag
  Correction will perform calculation on the fly
Well Data Annotation
Event: grad student pulled pressure transducers out of well.
Flag: invalid

## Slide 18
Non-timeseries Datasets
GIS & LiDAR
  5 LiDAR flights 2004,2009, (2014 green, 2015)
  10 years of GIS layers
Sensor Observatory
Geophysics: mapping fractured rock moisture
  Electrical Resistivity Tomography (ERT)
  Seismic refraction
  Neutron logging in wells
Targeted Field Campaigns
  Picarro CRDS analyzer in situ monitoring of d18O and dD in water & vapor
  Conservative tracer experiments during dry season
Manual Sampling and Monitoring
  Tracing isotopes through the system: vegetation, soil, lysimeter water, well, stream
  Well level hand measurements
  Collection of Isco water bottle samples
  Rain water collection
Automated water collection: chemical & isotope analysis
  Four 24 –position Isco water samplers: 3 wells, 1 stream
  Networked for remote sampling adjustment
  Modified bottle collectors to isolate water
New Tools
  Vadose-Zone-Monitoring System (VMS)
  Tree psychrometer
Notes: tree psychrometer: directly tests the relationships between moisture, lithology, and water balance in the dominant vegetation types

## Slide 19
CZO Data: Google Drive
CZO is required to archive research data and make it available after publication
What you need to archive
Raw data (no really. Raw as in unprocessed, messy, unformatted data)
Processed data
Methods for each step (sample method, cleaning method, analysis)
Goal: a stranger must be able to look at data, read your README files and use the data.
PowerPoints & Posters: also place CZO related media you give in Google Drive.

## Slide 20
Notes: Lessons Learned: low adoption of tools offered, need for time series

## Slide 21
• | Moderator introduction | Ben Galewsky (NCSA)
1 | CZO Cyberinfrastructure history | Collin Bode (CZO, UC Berkeley)
2 | Eel River CZO & Dendra | Collin
3 | IML CZO & Clowder+Geodashboard | Luigi Marini (CZO, NCSA)
4 | CUAHSI & HydroShare | Martin Seul (CUAHSI)
5 | Migrating CZO (meta)data to HydroShare | David Lubinski (CZO, CU-Boulder)
6 | “CZ Collaborative Network” NSF RFP | Luigi
• | Discussion | Ben
The Critical Zones: Supporting place-based research
Data management for the NSF Critical Zone Observatories program
SUMMER MEETING 2019
Notes: Transition from CZO-wide infrastructure to two Data Managers giving their perspective from the ground